## Slide 1: Analysis and Control Design Tools for Time-Delay Systems
Wim Michiels Department of Computer Science KU Leuven
ICINCO 2023 Conference, Rome 16 November 2023

## Slide 2: Outline
Applications and examples
Basic properties time-delay systems
Dimension reduction using predictor feedback
Dimension reduction using periodic feedback
  Switched periodic feedback
  Smooth periodic feedback
  Fixed-time observers
Time-delay methods in vibration control
Conclusions
Central theme: “beneficial effects of delays”

## Slide 3
Motivating examples
Synaptic time-delays
https://commons.wikimedia.org/wiki/File:
Blausen_0657_MultipolarNeuron.png
  networks
  - biology (e.g. interactions between neurons)
  - car following models
  - time-based spacing of airplanes
  - distributed and cooperative control, sensor networks
  - congestion control in communication networks
  mechanical engineering - machine tool vibrations (cutting and milling machines) - haptic interfaces and motion synchronization
  parallel computing (load balancing)
  population dynamics
  flow and propagation
  laser physics (lasers with optical feedback)

## Slide 4
Motivating examples
Goal: drive safely at small constant inter-vehicle distance
synchronization of the velocities is necessary
wireless communication of accelerations  time-delays
measurements inter-vehicle distances  time-delays
Cooperative driving
  networks
  - biology (e.g. interactions between neurons)
  - car following models
  - time-based spacing of airplanes
  - distributed and cooperative control, sensor networks
  - congestion control in communication networks
  mechanical engineering - machine tool vibrations (cutting and milling machines) - haptic interfaces and motion synchronization
  parallel computing (load balancing)
  population dynamics
  flow and propagation
  laser physics (lasers with optical feedback)
Source: TU/e - collaboration with Tue and TNO in framework of UCoCoS Training Network

## Slide 5
Motivating examples
  networks
  - biology (e.g. interactions between neurons)
  - car following models
  - time-based spacing of airplanes
  - distributed and cooperative control, sensor networks
  - congestion control in communication networks
  mechanical engineering - machine tool vibrations (cutting and milling machines) - haptic interfaces and motion synchronization
  parallel computing (load balancing)
  population dynamics
  flow and propagation
  laser physics (lasers with optical feedback)

## Slide 6
W: window-size
Q: queue length
N: number of TCP sessions
R: round-trip-time
C: link capacity
p: probability of packet mark
Tp: propagation delay
Sender
Receiver
Bottleneck
router
link c
rtt R
queue Q
acknowledgement
packet marking
  networks
  - biology (e.g. interactions between neurons)
  - car following models
  - time-based spacing of airplanes
  - distributed and cooperative control, sensor networks
  - congestion control in communication networks
  mechanical engineering - machine tool vibrations (cutting and milling machines) - haptic interfaces and motion synchronization
  parallel computing (load balancing)
  population dynamics
  flow and propagation
  laser physics (lasers with optical feedback)
Model Hollet et al (IEEE TAC’02)
Motivating examples

## Slide 7
  networks
  - biology (e.g. interactions between neurons)
  - car following models
  - time-based spacing of airplanes
  - distributed and cooperative control, sensor networks
  - congestion control in communication networks
  mechanical engineering - machine tool vibrations (cutting and milling machines) - haptic interfaces and motion synchronization
  parallel computing (load balancing)
  population dynamics
  flow and propagation
  laser physics (lasers with optical feedback)
Successive passages of teeth  delay
Rotation of each tooth  periodic coefficients
Delay inversely proportional to speed
Important: increase efficiency while avoiding undesired oscillations, so-called chatter
Principle of milling
Model
Motivating examples

## Slide 8
  networks
  - biology (e.g. interactions between neurons)
  - car following models
  - time-based spacing of airplanes
  - distributed and cooperative control, sensor networks
  - congestion control in communication networks
  mechanical engineering - machine tool vibrations (cutting and milling machines) - haptic interfaces and motion synchronization
  parallel computing (load balancing)
  population dynamics
  flow and propagation
  laser physics (lasers with optical feedback)
Heat Exchanger benchmark (CTU Prague)
Model: linear, dimension 6, five delays
Motivating examples

## Slide 9
Applications and examples
Basic properties time-delay systems
Dimension reduction using predictor feedback
Dimension reduction using periodic feedback
  Switched periodic feedback
  Smooth periodic feedback
  Fixed-time observers
Time-delay methods in vibration control
Conclusions
Outline

## Slide 10
x
0
t
Basics of time-delay systems
x
0
t
t1
x
0
t
Initial value problem

## Slide 11
0
µ
t=0
t=t1
t1
x
0
t1-¿
t
Ordinary differential equation on an infinite-dimensional function space

## Slide 12
Spectrum of linear time-invariant systems

## Slide 13
Delay systems are a class of distributed parameter systems /infinite-dimensional
Scalar examples:
oscillatory solutions
Analysis: complex behavior
Controller synthesis
chaotic attractor
Any control design problem involving the determinination of a finite number
of controller parameters is a reduced-order controller design problem
Induced limitations
Fundamental limitations (independent of controller)
Control design almost exclusively ends up in an optimization problems with hard trade-offfs to make

## Slide 14
Static state feedback applied to system with state and input delay

## Slide 15
TDS-CONTROL: An integrated MATLAB package for the analysis and controller-design
Stability by means of the characteristic roots and the spectral abscissa
Computation of zeros
Strong stability analysis of neutral delay differential equations, i.e., the effect of small delay pertubations can explicitly be taken into account.
Model order reduction and approximation
Stabilization by means of fixed-order dynamic output feedback controllers
Design of structured controllers like Pyragas, acceleration, PID controllers, decentralized and distributed controllers.
Performance and robust stability analysis by means of the H∞-norm, the pseudospectral abscissa, and the distance to instability.
Robust controller design through H∞-norm optimization.
System class
Functionality
Availability
Software https://gitlab.kuleuven.be/u0011378/tds-control
Documentation: P. Appeltans and W. Michiels. Analysis and controller design of time-delay systems using TDS-CONTROL. A tutorial and manual, E-print arXiv:2305.00341, 2023.
System
Controller
Matrix E is allowed to be singular: (delay) differential algebraic equations → modeling interconnected systems

## Slide 16
Beneficial effects of time-delays
Example 1. Stabilizing (coupled) oscillatory systems
Principle: use delay to adjust phase in accordance with oscillation
An extension:
Rightmost zeros of f simple and on imaginary axis:
Then: asymptotic stability for small k>0 (k<0)
If:
Characteristic equation
Condiiton = use delay to adjust phase in accordance with all oscillatory modes
Applications: stabilization of networks of oscillators, gyroscopic systems
(Number of Unstable roots)

## Slide 17
Example 2. Generating predictions and stabilizing predictors
Predictor over a time-interval of length :
Autonomous system
unstable if origin not stable
initialization??

## Slide 18
is a prediction of x  x is a delayed version of z
stabilization mechanism:
Prediction error satisfies
 predictor is stable if the zero solution of (1) is stable;
determining K: stabilization problem with delayed feedback
Example 2. Generating predictions and stabilizing predictors
Predictor over a time-interval of length :
Autonomous system

## Slide 19
Example 3. State reconstruction, approximation of missing derivatives
Example 4. Making the control law non-invasive
Goal: stabilizing an unstable periodic orbit with period T
Principles
Stabilization of minimum-phase systems with delayed output feedback
control low based on derivative feedback
approximate derivatives by finite differences
apply scaling property ( high gains, small delays )
Application: class of proportional-delayed controllers

## Slide 20: Outline
Applications and examples
Basic properties time-delay systems
Dimension reduction using predictor feedback
Dimension reduction using periodic feedback
  Switched periodic feedback
  Smooth periodic feedback
  Fixed-time observers
Time-delay methods in vibration control
Conclusions

## Slide 21
Delay compensation by prediction
→ “finite-dimensional” design problem

## Slide 22
+
-
+
-
-

## Slide 23
Properties

## Slide 24: Outline
Applications and examples
Basic properties time-delay systems
Dimension reduction using predictor feedback
Dimension reduction using periodic feedback
  Switched periodic feedback
  Smooth periodic feedback
  Fixed-time observers
Time-delay methods in vibration control
Conclusions

## Slide 25
Act-and-wait control

## Slide 26
Potential for direct eigenvalue placement of monodromy matrix
Potential for fixed-time stability / deadbeat response

## Slide 27
Potential for fixed-time stability (II)
Limitations induced by delay
Can these limitations be overcome?

## Slide 28
What about a time-varying periodic gain?
periodic

## Slide 29
Fixed-time stabilization
Open loop phases?

## Slide 30
Towards observation in a prescribed time
design parameter
Potential
to arrive at systems with provable guarantees (formal methods in control)
Hierarchical control / reduction techniques

## Slide 31
Applications and examples
Basic properties time-delay systems
Dimension reduction using predictor feedback
Dimension reduction using periodic feedback
  Switched periodic feedback
  Smooth periodic feedback
  Fixed-time observers
Time-delay methods in vibration control
Conclusions
Outline
Collaboration group T. Vyhlídal, CTU (joint PhDs D. Pilbauer, A. Sandanha)

## Slide 32
Goal: avoid excitation at given frequency, , by filtering
Feedforward solution:
Feedback solution:
Simplest form of shaper
Input shaping

## Slide 33
Non-collocated vibration suppression using the delayed resonator
Collocated case: target is accessible
Tuned Vibration Absorber added to suppress vibrations of target at given frequency 
Principle: anti-resonance
Delayed resonator
with gain g and delay  as controller parameters
Non-collocated vibration suppression using the delayed resonator
Harmonic disturbance
Target

## Slide 34
Non-collocated suppression (level I)
Non-collocated suppression (level II)
Principle of non-collocated vibration suppression
Target
Harmonic disturbance
Harmonic disturbance
Target
resonating substructure
resonating substructure

## Slide 35
Methodology
Two control loops (2 delays + 2 gains)
→ vibration suppression
→ ensure closed-loop stability with sufficient margin
Inter-dependence between the controllers
Harmonic disturbance
Target
Parameter tuning:
- mimimize the spectral abscissa of closed-loop system
- subject to zero location constraints on transfer function from d to target’s position
Using software integrated in TDS-CONTROL

## Slide 36
36
Harmonic disturbance
Target
Harmonic disturbance
Target
Experimental validation

## Slide 37: Conclusions
A control-oriented overview of time-delay systems, with focus on
  beneficial effect of delays / use of delays for control
  solutions to control problem in the form of explicit feedback laws
Two finite-dimensional representations of closed-loop systems with delay, induced by structure of the controller
Outlook: incorporate compact but informative time-delay models in data-driven modeling and control strategies
References Michiels, W. (2020). Control of Linear Systems with Delay. In: Encyclopedia of Systems and Control, 2nd Edition
Michiels, W., Zhou, B. (2020). On the fixed-time stabilization of input delay systems using act-and-wait control. Systems & Control Letters.
Silm, H., Kure, M., Busek, J., Michiels, W., Vyhlidal, T. with Michiels, W. (2023). Spectral design and experimental validation of non- collocated vibration suppression by a delayedresonator and time-delay controller. IEEE Transactions on Control Systems Technology.
Zhou, B., Michiels, W., Chen, J. (2022). Fixed-time stabilization of linear delay systems by smooth periodic delayed feedback. IEEE Transactions On Automatic Control.