## Slide 1: Deep Learning for Active Robotic Perception
Nikolaos Passalis, Pavlos Tosidis, Theodoros Manousis,
and Anastasios Tefas
Presenter: Prof. Anastasios Tefas
Department of Informatics, Aristotle University of Thessaloniki, Thessaloniki, Greece
IJCCI 2023 - 15th International Joint Conference on Computational Intelligence

## Slide 2: Structure
Deep Learning Challenges in Robotics
  Introduction
  Deep Active Perception
    Overview
    Supervised Deep Active Perception
    RL-based Active Perception
  Lightweight Intelligence for Robotics
OpenDR: An Open Deep Learning toolkit for Robotics
Interconnected

## Slide 3: Deep Learning and Challenges
Deep Learning led to state-of-the-art performance in perception and cognition
Steep Learning Curve
Difficult for robotics laboratories/companies to employ deep learning methodologies to their research/products
Computational complexity
DL requires powerful and specialized hardware which makes using DL models on embedded systems difficult
Passive Perception
Traditional Computer Vision approaches do not consider the interaction between a robot and the world
Deep Learning in robotics and related areas leads to hurdles, requirements and research questions that are not fully addressed within the deep learning community

## Slide 4: Deep Learning and Challenges in Robotics
Overcoming the learning curve barrier
Overcoming the computational complexity barrier
Overcoming the passive perception barrier
A toolkit with a collection of ROS nodes and the necessary tools for training and deployment is being developed that will enable any ROS-based robotic architecture to easily integrate them for improving its technical capabilities.
State-of-the-art lightweight deep learning models are developed. Models provide real-time inference on embedded systems, while being able to process high-resolution data.
A complete framework for simulating and developing robotics applications that use deep learning methodologies is developed.
Tools for enhanced robot navigation, action and manipulation capabilities are developed.

## Slide 5: Active Perception
Robots can interact with the environment to better sense their surroundings
e.g., consider the task of face recognition
  A robot might acquire a sub-optimal profile view of a subject
  Existing static perception-based DL models might fail to recognize the subject from this view
  This is especially true if it has never been trained on profile face images
  However, a robot can acquire a better and more discriminative view by appropriately repositioning itself with respect to the human subject
  In this case, the exact same DL model, will probably be able to recognize the subject

## Slide 6: Active Perception
It is worth noting that this process is very similar to the way humans and various animals interact and understand their environment
For example, humans tend to look from different angles when trying to process complex visual stimuli, while many mammals have specialized muscles that rotate their ears toward the source of an audio signal
Despite this, most DL models currently do not employ active perception strategies

## Slide 7: Active Perception
Can the recognition accuracy of DL models be improved by acquiring a more appropriate view, after manipulating the position of a robot inside the world?
  For example, moving a robot closer to a human is expected to improve the confidence of the robot when recognizing a human, as well as reduce the recognition errors

## Slide 8: Active Perception
A significant part of the complexity in modern DL models might arise from their ability to perform view invariant inference.
  Can you read upside down?
  Significantly smaller models can be used when active perception approaches are employed, without reducing recognition accuracy.

## Slide 9: Active Perception

## Slide 10: Active Perception

## Slide 11: Active Perception for Embedding-based Face Recognition
N. Passalis, A. Tefas, Leveraging Active Perception for Improving Embedding-based Deep Face Recognition, MMSP 2020
Learn how to control the camera to maximize the confidence of the recognition for database-based face recognition

## Slide 12: Active Perception for Embedding-based Face Recognition
N. Passalis, A. Tefas, Leveraging Active Perception for Improving Embedding-based Deep Face Recognition, MMSP 2020

## Slide 13: Occlusion Removal using Active Perception
Lack of occlusion-oriented active perception datasets
Synthetic Generation Approach using large-scale datasets (COCO, MS Celeb)
Integrating simulation and training
V. Dimaridou, N. Passalis and A. Tefas, DEEP ACTIVE ROBOTIC PERCEPTION FOR IMPROVING FOR FACE RECOGNITION UNDER OCCLUSIONS (Accepted, SSCI 2023)

## Slide 14: Occlusion Removal using Active Perception
V. Dimaridou, N. Passalis and A. Tefas, DEEP ACTIVE ROBOTIC PERCEPTION FOR IMPROVING FOR FACE RECOGNITION UNDER OCCLUSIONS (Accepted, SSCI 2023)
Two-step process
  First step: Decide if active perception is needed and the direction of movement
  Needs to be fast, runs at every inference step

## Slide 15: Occlusion Removal using Active Perception
V. Dimaridou, N. Passalis and A. Tefas, DEEP ACTIVE ROBOTIC PERCEPTION FOR IMPROVING FOR FACE RECOGNITION UNDER OCCLUSIONS (Accepted, SSCI 2023)
Two-step process
  Second step: Perform a trial movement and infer the rest of the movement
  Platform-agnostic
  Enables efficient planning

## Slide 16: Occlusion Removal using Active Perception
V. Dimaridou, N. Passalis and A. Tefas, DEEP ACTIVE ROBOTIC PERCEPTION FOR IMPROVING FOR FACE RECOGNITION UNDER OCCLUSIONS (Accepted, SSCI 2023)
Can recover face verification accuracy in just two steps!

## Slide 17: Active Vision Control Policies for Face Recognition using Deep Reinforcement Learning
Pavlos Tosidis, Nikolaos Passalis, Anastasios Tefas “ACTIVE VISION CONTROL POLICIES FOR FACE RECOGNITION USING DEEP REINFORCEMENT LEARNING” , EUSIPCO 2022
A DRL agent is employed to issue control commands to acquire the most appropriate view for improving face recognition accuracy
Lightweight agent
  180 FPS on Nvidia RTX2070, deploys face detection/recognition only when confident enough for success.
Reward based on face recognition

## Slide 18: Active Vision Control Policies for Face Recognition using Deep Reinforcement Learning
Pavlos Tosidis, Nikolaos Passalis, Anastasios Tefas “ACTIVE VISION CONTROL POLICIES FOR FACE RECOGNITION USING DEEP REINFORCEMENT LEARNING” , EUSIPCO 2022
Evaluation results on two scenarios

## Slide 19: Active Perception in Real Use Cases (Active)

## Slide 20: High-resolution Pose Estimation
T. Manousis, N. Passalis, and A. Tefas, “ENABLING HIGH-RESOLUTION POSE ESTIMATION IN REAL TIME USING ACTIVE PERCEPTION”, ICIP 2023
The proposed methodology consists of two basic steps:
Step 1: First we downscale the input image and pass it from the bottom-up model to generate a heatmap with the approximate location of humans.
Step 2: Apply pose-estimation model on a specific area of the high-resolution input image as detected in “Step 1”

## Slide 21: Active Perception in Real Use Cases

## Slide 22: High-resolution Pose Estimation
T. Manousis, N. Passalis, and A. Tefas, “ENABLING HIGH-RESOLUTION POSE ESTIMATION IN REAL TIME USING ACTIVE PERCEPTION”, ICIP 2023
Since the purpose of the research is focused on the high-resolution images, we created three new image datasets based on COCO2017
The original COCO2017 images are placed on a larger resolution canvas
  1280x720 (720p)
  1920x1080 (1080p)
  2560x1440 (1440p)
The proposed method can be applied by using any bottom-up pose estimation approach
For this research Lightweight OpenPose was used

## Slide 23: High-resolution Pose Estimation
T. Manousis, N. Passalis, and A. Tefas, “ENABLING HIGH-RESOLUTION POSE ESTIMATION IN REAL TIME USING ACTIVE PERCEPTION”, ICIP 2023
In the table below we present the average precision (0.5:0.95) results of the LightWeight OpenPose and the proposed method on different input size datasets
In the following table we demonstrate how the image resolution on the second pass, affects the results of proposed method. We conducted 3 experimental setups with different resolution.
Setup 1: 360 pixels
Setup 2: 540 pixels
Setup 3: 720 pixels

## Slide 24: Trajectory-based Active Object Detection
Co-integrated Simulation and Learning to determine optimal active perception trajectories
Grid-search to infer optimal trajectories
Train a DL model to provide navigation proposals
S. Ginargyros, N. Passalis, A. Tefas “ Deep Active Perception for Object Detection using Navigation Proposals” , SSCI 2023 (accepted)

## Slide 25: Trajectory-based Active Object Detection
S. Ginargyros, N. Passalis, A. Tefas “ Deep Active Perception for Object Detection using Navigation Proposals” , SSCI 2023 (accepted)
Co-integrated Simulation and Learning to determine optimal active perception trajectories
Confidence heatmaps can also increase the explainability of models

## Slide 26: Trajectory-based Active Object Detection
S. Ginargyros, N. Passalis, A. Tefas “ Deep Active Perception for Object Detection using Navigation Proposals” , SSCI 2023 (accepted)
Evaluate three different approaches: a) regressing the best position, b) performing classification towards the direction of movement and c) performing random movements

## Slide 27: Leveraging Deep Reinforcement Learning for Active Shooting Under Open-World Setting
Preliminary work aiming to examine whether RL can be used in challenging open world and unconstrained settings to acquire more informative views
AirSim-based simulation, DRL trained on raw RGB input
Reward: distance + view based
A. Tzimas, N. Passalis, and A. Tefas, Leveraging Deep Reinforcement Learning for Active Shooting Under Open-World Setting, ICME 2020

## Slide 28: Visual Question Answering through Active Perception
The effect of active perception was simulated on a VQA dataset using crop/translation/zoom operations
A RL agent was trained to maximize the confidence on providing the correct answer
T. Bozinis, N. Passalis and A. Tefas, Improving Visual Question Answering using Active Perception on Static Images, ICPR 2020

## Slide 29: Visual Question Answering through Active Perception
T. Bozinis, N. Passalis and A. Tefas, Improving Visual Question Answering using Active Perception on Static Images, ICPR 2020

## Slide 30: Visual Question Answering through Active Perception
T. Bozinis, N. Passalis and A. Tefas, Improving Visual Question Answering using Active Perception on Static Images, ICPR 2020

## Slide 31: Pseudo-active Vision for Improving Deep Visual Perception
DL models are especially sensitive to different illumination conditions
Solutions:
  Train with data augmentation (usually more parameters needed)
  Control the camera parameters (slow, increases the latency)
  Proposed: Learn how to transform the input data distribution in order to match the distribution the DL model expects
N. Passalis, A. Tefas, Pseudo-active Vision for Improving Deep Visual Perception through Neural Sensory Refinement, ICIP 2021

## Slide 32: Pseudo-active Vision for Improving Deep Visual Perception
N. Passalis, A. Tefas, Pseudo-active Vision for Improving Deep Visual Perception through Neural Sensory Refinement, ICIP 2021

## Slide 33: Active Perception and Continual Learning
Can we incorporate effortlessly active and continual learning into existing FR pipelines to improve existing FR systems’ performance?
Will a system be more accurate on recognizing a person, using informative samples gathered during inference to augment its database?
Simple, yet effective approach
  Manipulate the reference representations stored for the identities to be recognized
P. Tosidis, N. Passalis, A. Tefas, LEVERAGING ACTIVE AND CONTINUAL LEARNING FOR IMPROVING DEEP FACE RECOGNITION IN-THE-WILD, MMSP

## Slide 34: Active Perception and Continual Learning
P. Tosidis, N. Passalis, A. Tefas, LEVERAGING ACTIVE AND CONTINUAL LEARNING FOR IMPROVING DEEP FACE RECOGNITION IN-THE-WILD, MMSP 2023
Typical FR pipeline
Proposed

## Slide 35: Active Perception in Real Use Cases

## Slide 36: Active Perception in Real Use Cases

## Slide 37: Lightweight Deep Learning
Lightweight Architectures
Neural Network Distillation
Appropriate Regularization
Quantization
Adaptive Inference
…

## Slide 38: Quadratic Mutual Information Regularization in Real-time Deep CNN Models
Lightweight VGG-based CNN models able to run in real-time on Jetson-TX2 for high resolution input (720p and 1080p)
Regularization, e.g., based on the Quadratic Mutual Information criterion, can be used to enhance the generalization ability of the proposed models
- M. Tzelepi and A. Tefas, Quadratic Mutual Information Regularization in Real-Time Deep CNN Models, MLSP 2020
- M. Tzelepi and A. Tefas, Improving the performance of lightweight CNNs for binary classification using Quadratic Mutual Information regularization, Pattern Recognition 2020

## Slide 39: Quadratic Mutual Information Regularization in Real-time Deep CNN Models
Heatmap on high-resolution drone-captured image considering the task of football player detection, utilizing the proposed regularized real-time on input of resolution 1080p CNN model.
- M. Tzelepi and A. Tefas, Quadratic Mutual Information Regularization in Real-Time Deep CNN Models, MLSP 2020
- M. Tzelepi and A. Tefas, Improving the performance of lightweight CNNs for binary classification using Quadratic Mutual Information regularization, Pattern Recognition 2020

## Slide 40: Knowledge Distillation
Knowledge distillation (KD) allows for improving the performance of lightweight DL models
KD works by using a larger teacher model to guide the training of a lightweight student model
Several different KD methods can be used accounting for the different scenarios that often occur:
  Online and Self Distillation
  Distillation from Teacher Ensembles
  Multi-level Distillation

## Slide 41: Online Self-Acquired Knowledge Distillation
Acquires soft labels
  from the model itself
  in an online manner
The proposed method does not require the utilization of multiple models or copies of the model like the most online KD methods, rendering it more efficient
The proposed method is model-agnostic
- M. Tzelepi and A. Tefas, Efficient Training of Lightweight Neural Networks Using Online Self-Acquired Knowledge Distillation, ICME 2021
- M. Tzelepi and A. Tefas, Online Self-Acquired Knowledge Distillation, Submitted

## Slide 42: Heterogeneous Knowledge Distillation using Information Flow Modeling
Transferring the knowledge encoded in a large and complex neural network into a smaller and faster one, considering the way information flows through the intermediate layers
N. Passalis, M. Tzelepi, and A. Tefas, Heterogeneous Knowledge Distillation using Information Flow Modeling, CVPR, 2020

## Slide 43: Heterogeneous Knowledge Distillation using Information Flow Modeling
N. Passalis, M. Tzelepi, and A. Tefas, Heterogeneous Knowledge Distillation using Information Flow Modeling, CVPR, 2020

## Slide 44: Knowledge Distillation using Unified Ensembles of Specialized Teachers
Instead of performing distillation from one single model, we constructed an ensemble of class-specialized teachers
Each teacher specializes in one sub-set of the classes
This ensemble is trained in a unified way to increase the efficiency (instead of training separate models)
A. Zaras, N. Passalis, A. Tefas, Improving Knowledge Distillation using Unified Ensembles of Specialized Teachers, Pattern Recognition Letters 2021

## Slide 45: Adaptive Inference Models for Classification
In many cases we can make "early" decisions in DL models, especially for easier input samples
Using BoF-based early exits can allow for reducing the computational requirements
Contributions:
  BoF aggregation
  Re-use previous representations
  Use additive representations
  Robust confidence estimation
- N. Passalis, J. Raitoharju, A. Tefas, and M. Gabbouj, Efficient adaptive inference for deep convolutional neural networks using hierarchical early exits, Pattern Recognition, 2020
- N. Passalis, J. Raitoharju, M. Gabbouj, and A. Tefas, Efficient Adaptive Inference leveraging Bag-of-Features-based Early Exits, MMSP 2020

## Slide 46: Adaptive Inference Models for Metric Learning
Difficult to apply in representation/metric learning setting
Representations can be directly used, but these often have different dimensionality per layer
  Increased space requirements
  Lower accuracy
Use the Bag-of-Features model to efficiently extract compact representations from any layer of a DL model that is then combined with an efficient linear regressor to match the final representation of the model
  Maps the intermediate feature spaces into the final one, instead of working in these spaces
N. Passalis and A. Tefas, Adaptive Inference for Face Recognition leveraging Deep Metric Learning-enabled Early Exits, EUSIPCO 2021

## Slide 47: OpenDR toolkit
An Open Toolkit for providing Active Perception capabilities

## Slide 48: Deep Learning and Challenges
Deep Learning led to state-of-the-art performance in perception and cognition
Steep Learning Curve
Difficult for robotics laboratories/companies to employ deep learning methodologies to their research/products
Computational complexity
DL requires powerful and specialized hardware which makes using DL models on embedded systems difficult
Passive Perception
Traditional Computer Vision approaches do not consider the interaction between a robot and the world
Deep Learning in robotics and related areas leads to hurdles, requirements and research questions that are not fully addressed within the deep learning community

## Slide 49: Deep Learning and Challenges in Robotics
Overcoming the learning curve barrier
Overcoming the computational complexity barrier
Overcoming the passive perception barrier
A toolkit with a collection of ROS nodes and the necessary tools for training and deployment is being developed that will enable any ROS-based robotic architecture to easily integrate them for improving its technical capabilities.
State-of-the-art lightweight deep learning models are developed. Models provide real-time inference on embedded systems, while being able to process high-resolution data.
A complete framework for simulating and developing robotics applications that use deep learning methodologies is developed.
Tools for enhanced robot navigation, action and manipulation capabilities are developed.

## Slide 50: OpenDR Main Objective
To develop a modular, open, and non-proprietary toolkit for core robotic functionalities by harnessing deep learning to provide advanced perception and cognition capabilities, meeting in this way the general requirements of robotics applications in different areas.

## Slide 51: OpenDR Ecosystem and Development

## Slide 52: OpenDR Active Perception Specifications

## Slide 53: OpenDR Use Cases
Healthcare Robotics
Robots supporting elderly people

## Slide 54: OpenDR Use Cases
Agricultural Robotics
Intelligent Mechanical Weeding

## Slide 55: OpenDR Use Cases
Agile Production
Human-robot collaborative Diesel engine assembly

## Slide 56: OpenDR at a glance
H2020 Research and Innovation Action
Coordinated by
Aristotle University of Thessaloniki
Prof. Anastasios Tefas
tefas@csd.auth.gr
8 partners from 7 European countries
Duration: 48 months (ends: 31-12-2023)

## Slide 57
Academic partners:
Aristotle University Thessaloniki (GR)
Tampere University (FN)
Aarhus University (DK)
Delft University of Technology (NL)
University of Freiburg (DE)
Industrial partners:
Cyberbotics (CH)
PAL Robotics (ES)
AgroIntelli (DK)

## Slide 58: Current Status
Active development
First version of OpenDR released on 31 Dec 2021!
6 releases already!

## Slide 59: Current Status
Available through major distribution channels:
  pip package
  Docker images for various platforms
  Support for Jetson TX-2, NX, AGX (pre-release)
  Github source distribution
v.1.1 also provides more flexible installation options (installing only parts of the toolkit)

## Slide 60: Current Status
Several tools already available

## Slide 61: Current Status
Several tools already available

## Slide 62: Conclusions
Active Perception holds the credentials for unlocking next-gen DL-enabled robotic perception capabilities
  Shift in training and deployment pipelines
  Supervised learning approaches require solving proxy problems (might lead to suboptimal results), yet are easier to train
  DRL can be directly used in active perception scenarios, yet more difficult to train
  On-board deployed is almost always required, leading to the need for lightweight DL models

## Slide 63: More Info / Contact
Find more about OpenDR
www.opendr.eu
github.com/opendr-eu/opendr
Project Coordinator: Prof. Anastasios Tefas
E-mail: tefas@csd.auth.gr

## Slide 64: Thank you! Questions?