## Slide 1: An analysis of power-to-X technologies in modern district energy networks Francesco Calise Department of industrial engineering University of Naples FEDERICO II
12th International Conference on Smart Cities and Green ICT Systems
SMARTGREENS2023

## Slide 2: Outline
Present Scenario and perspectives by 2050
Energy Transition and related Policies
Novel Energy Networks
District Heating and Cooling Networks
Smart Grids
Power-to-x
  Power to fuel
  Power to gas
  Power to heat
  Power to Power
Research and Development
Conclusions

## Slide 3: CO2 emissions and temperature increase
“Dear friends, humanity is on thin ice and that ice is melting fast. As today’s report of the Intergovernmental Panel on Climate Change (IPCC) details, humans are responsible for virtually all global heating over the last 200 years. The rate of temperature rise in the last half century is the highest in 2,000 years. Concentrations of carbon dioxide are at their highest in at least 2 million years. The climate time-bomb is ticking”
UN Secretary-General António Guterres, March 2023
Source: IPCC 2022
Shared Socioeconomic
Pathways (SSP)
Radiative forcing is the change in the balance between radiation coming into the atmosphere and radiation going out.
3

## Slide 4: GDP growth rates projections
Statistical Department of US Department of Energy
Chart: 
| total OECD |  | Japan | South Korea | OECD Europe | Canada | United States | Mexico and Other Americas | Australia and New Zealand
growth rate | 0.017202 | 0 | 0.0039976 | 0.011199 | 0.015099 | 0.019103 | 0.021466 | 0.022017 | 0.022095
Chart: 
| total non-OECD |  | Brazil | Russia | Middle East | Other Americas | Other Europe and Eurasia | China | Africa | Other Asia | India
growth rate | 0.03546 | 0 | 0.012547 | 0.014195 | 0.022357 | 0.031363 | 0.032676 | 0.033089 | 0.03323 | 0.038553 | 0.053662
Average annual percentage change in GDP, OECD
2020–2050
Average annual percentage change in GDP, non-OECD
2020–2050
GDP is expected to grow by 2050 (annual percentage change ranging from 1.5 to 3.5 %, depending on the area). For developed Countries the increase is limited whereas it may be significantly high for developing regions (e.g., Africa). This increase in GDP must be SUSTAINABLE for the environment and mankind.

## Slide 5: GDP and energy consumption
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
series1 | 48.6717 | 49.6963 | 50.3734 | 51.1961 | 52.3202 | 53.6956 | 54.6842 | 56.1433 | 57.4748 | 58.4074 | 55.4065 | 57.7981 | 60.6688 | 62.7473 | 64.3733 | 65.8924 | 67.3159 | 68.6987 | 70.1087 | 71.4826 | 72.8792 | 74.2802 | 75.7307 | 77.3241 | 78.9376 | 80.5658 | 82.1493 | 83.7367 | 85.3925 | 87.1132 | 88.8485 | 90.5922 | 92.3344 | 94.1157 | 95.9207 | 97.7575 | 99.6668 | 101.6106 | 103.6041 | 105.6148 | 107.6943
series2 | 48.6717 | 49.6963 | 50.3734 | 51.1961 | 52.3202 | 53.6956 | 54.6842 | 56.1433 | 57.4748 | 58.4074 | 55.1798 | 56.7773 | 58.8193 | 60.0362 | 60.882 | 61.6303 | 62.3204 | 62.9897 | 63.6609 | 64.265 | 64.8793 | 65.5145 | 66.2121 | 66.903 | 67.5663 | 68.2308 | 68.854 | 69.4599 | 70.089 | 70.766 | 71.5017 | 72.1787 | 72.8326 | 73.5213 | 74.2532 | 74.978 | 75.6247 | 76.2758 | 76.9989 | 77.7126 | 78.4374
series4 | 45.5166 | 48.2551 | 50.704 | 53.225 | 55.6657 | 57.8889 | 60.5178 | 63.3621 | 66.2633 | 68.7489 | 67.1496 | 72.3417 | 76.9048 | 81.3119 | 85.8551 | 90.5178 | 95.2473 | 100.1277 | 105.1965 | 110.4694 | 115.9207 | 121.5186 | 127.2328 | 133.0745 | 139.2055 | 145.3048 | 151.4543 | 157.7834 | 164.3143 | 171.0403 | 177.9161 | 184.8896 | 192.0563 | 199.4552 | 206.9699 | 214.8006 | 222.7285 | 231.2305 | 239.443 | 247.2726 | 255.4334
series5 | 45.5166 | 48.2551 | 50.704 | 53.225 | 55.6657 | 57.8889 | 60.5178 | 63.3621 | 66.2633 | 68.7489 | 67.1507 | 70.9352 | 73.8384 | 76.6263 | 79.4227 | 82.1855 | 84.9358 | 87.6644 | 90.3779 | 93.0687 | 95.7467 | 98.4313 | 101.0777 | 103.6651 | 106.1898 | 108.6838 | 111.1226 | 113.5299 | 115.928 | 118.3289 | 120.7354 | 123.1005 | 125.4449 | 127.7822 | 130.1056 | 132.3874 | 134.5554 | 136.6838 | 138.7912 | 140.8471 | 142.8487
series0 | 48.6717 | 49.6963 | 50.3734 | 51.1961 | 52.3202 | 53.6956 | 54.6842 | 56.1433 | 57.4748 | 58.4074 | 55.289 | 57.3145 | 59.745 | 61.3452 | 62.5809 | 63.7536 | 64.8412 | 65.8603 | 66.8437 | 67.799 | 68.8039 | 69.8445 | 70.9051 | 71.9903 | 73.1159 | 74.2344 | 75.3039 | 76.3596 | 77.4456 | 78.5659 | 79.7191 | 80.8873 | 82.1004 | 83.3424 | 84.5891 | 85.835 | 87.076 | 88.3215 | 89.6091 | 90.9178 | 92.2272
series3 | 45.5166 | 48.2551 | 50.704 | 53.225 | 55.6657 | 57.8889 | 60.5178 | 63.3621 | 66.2633 | 68.7489 | 67.1507 | 71.5916 | 75.3423 | 78.9631 | 82.6301 | 86.3436 | 90.1065 | 93.8916 | 97.719 | 101.6001 | 105.5508 | 109.5746 | 113.6155 | 117.6779 | 121.7579 | 125.8659 | 129.9625 | 134.0749 | 138.233 | 142.4556 | 146.7343 | 151.0473 | 155.4258 | 159.8635 | 164.3379 | 168.827 | 173.2638 | 177.6984 | 182.142 | 186.586 | 191.0059
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
series1 | 246.1195 | 243.8506 | 241.5248 | 244.2872 | 243.1432 | 243.7933 | 244.965 | 247.1893 | 250.3148 | 250.6621 | 232.9328 | 240.2145 | 245.0607 | 248.7346 | 251.3978 | 253.3107 | 254.6815 | 255.9805 | 257.6132 | 259.4294 | 261.2136 | 263.0803 | 265.0655 | 267.1419 | 269.5961 | 272.1224 | 274.4371 | 276.7457 | 279.1179 | 281.5813 | 284.1252 | 286.9372 | 289.7539 | 292.6718 | 295.596 | 298.5195 | 301.4756 | 304.6806 | 307.8976 | 311.0643 | 314.5303
series2 | 246.1195 | 243.8506 | 241.5248 | 244.2872 | 243.1432 | 243.7933 | 244.965 | 247.1893 | 250.3148 | 250.6621 | 232.9361 | 237.6085 | 240.3108 | 242.2847 | 242.9762 | 243.0209 | 242.5399 | 242.2077 | 242.1513 | 242.3479 | 242.4304 | 242.569 | 242.9869 | 243.3247 | 243.9023 | 244.4983 | 244.845 | 245.168 | 245.4727 | 245.9757 | 246.516 | 247.1495 | 247.7592 | 248.5315 | 249.3084 | 250.1402 | 250.7225 | 251.5653 | 252.5257 | 253.3741 | 254.4285
series4 | 295.4535 | 312.2453 | 326.8189 | 333.9728 | 340.5294 | 340.8405 | 341.3701 | 355.2319 | 369.1431 | 382.2464 | 368.6409 | 387.4873 | 401.4538 | 413.5196 | 425.1728 | 436.1027 | 446.8647 | 457.0668 | 467.8024 | 478.3443 | 489.2244 | 501.172 | 513.3339 | 525.2435 | 537.7888 | 550.0707 | 563.0667 | 576.1469 | 589.5233 | 602.6678 | 616.3503 | 629.8015 | 643.535 | 657.6621 | 671.3186 | 685.2959 | 698.9462 | 713.503 | 727.3117 | 740.6802 | 754.181
series5 | 295.4535 | 312.2453 | 326.8189 | 333.9728 | 340.5294 | 340.8405 | 341.3701 | 355.2319 | 369.1431 | 382.2464 | 368.6184 | 382.5724 | 390.0661 | 395.6194 | 400.8332 | 405.302 | 409.3113 | 412.6268 | 416.1537 | 419.3187 | 422.5503 | 426.1989 | 429.9739 | 433.3326 | 437.0382 | 440.4057 | 444.1998 | 447.8844 | 451.7087 | 455.2096 | 459.1346 | 462.7841 | 466.4427 | 470.3349 | 473.8424 | 477.2388 | 479.7124 | 482.3183 | 484.6258 | 486.9933 | 489.2508
series0 | 246.1195 | 243.8506 | 241.5248 | 244.2872 | 243.1432 | 243.7933 | 244.965 | 247.1893 | 250.3149 | 250.6617 | 232.9187 | 238.9409 | 242.8607 | 245.3524 | 246.8812 | 247.9629 | 248.477 | 248.8795 | 249.5627 | 250.4911 | 251.3289 | 252.4839 | 253.6216 | 254.769 | 256.2627 | 257.7265 | 258.8858 | 260.0799 | 261.2442 | 262.5128 | 263.7667 | 265.2591 | 266.8783 | 268.6221 | 270.2712 | 271.9676 | 273.6374 | 275.4316 | 277.3364 | 279.1768 | 281.2746
series3 | 295.4535 | 312.2453 | 326.8189 | 333.9728 | 340.5294 | 340.8405 | 341.3701 | 355.2319 | 369.1431 | 382.2448 | 368.6058 | 384.6229 | 395.1623 | 403.8144 | 412.0611 | 419.5843 | 426.913 | 433.5624 | 440.49 | 447.0955 | 453.9143 | 461.4174 | 469.123 | 476.4332 | 484.2326 | 491.7328 | 499.7065 | 507.6205 | 515.6784 | 523.4577 | 531.6511 | 539.4186 | 547.2838 | 555.4405 | 563.169 | 570.7854 | 577.739 | 584.8421 | 591.5493 | 598.3663 | 605.0523
World GDP
trillion 2015 dollars, purchasing power parity (PPP)
Energy consumption
quadrillion British thermal units
Source: EIA 2021
The growth in GDP is strictly related to the increase in the overall primary energy demand, required to support the development. For developed Countries, a limited increase in primary energy demand is expected, due to the recent policies in terms of climate change. Conversely, for developing Countries a dramatic growth in primary energy demand is expected. Therefore, urgent actions must be implemented to prevent a dramatic environmental impact of this growth.

## Slide 6: World energy consumption by sector and fuel
Source: EIA 2021
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Transportation | 103.1629 | 104.9714 | 106.2922 | 108.7067 | 110.9338 | 113.3851 | 116.2358 | 118.4976 | 120.6542 | 123.1961 | 107.7755 | 114.6184 | 120.0603 | 123.1418 | 125.0838 | 126.7401 | 127.9282 | 128.9258 | 129.9501 | 130.896 | 131.8694 | 132.8296 | 133.7943 | 134.7618 | 135.8315 | 136.9364 | 138.039 | 139.1182 | 140.2306 | 141.4651 | 142.6596 | 144.0065 | 145.3257 | 146.7103 | 148.0487 | 149.4577 | 150.6867 | 152.0183 | 153.31 | 154.6144 | 155.8852
Industrial | 219.6081 | 228.0594 | 235.5113 | 235.9072 | 238.4937 | 237.3676 | 237.1197 | 243.7613 | 248.2946 | 250.0838 | 240.9891 | 253.7303 | 259.447 | 264.1468 | 268.0669 | 271.822 | 275.6164 | 279.1673 | 282.8301 | 286.5452 | 290.3547 | 294.2688 | 297.9781 | 301.6503 | 305.495 | 309.2733 | 312.9952 | 316.6257 | 320.2649 | 323.8812 | 327.433 | 330.945 | 334.6068 | 338.2674 | 341.7527 | 345.1456 | 348.449 | 351.6806 | 354.8616 | 358.1074 | 361.3137
Commercial | 29.5 | 29.6641 | 29.9433 | 31.1138 | 31.0678 | 31.8894 | 32.1147 | 32.7963 | 33.7409 | 34.0437 | 33.1308 | 33.6187 | 34.1092 | 34.6428 | 35.1813 | 35.6198 | 36.0929 | 36.4417 | 36.8269 | 37.2488 | 37.6442 | 37.9624 | 38.3386 | 38.7042 | 39.1074 | 39.5082 | 39.9298 | 40.3334 | 40.7603 | 41.1593 | 41.6559 | 42.0643 | 42.4625 | 42.9574 | 43.3772 | 43.7977 | 44.1576 | 44.5719 | 45.0208 | 45.3748 | 45.8304
Residential | 55.6565 | 55.7619 | 55.6333 | 57.4778 | 57.4178 | 57.7535 | 58.2401 | 59.9794 | 62.9243 | 63.8571 | 63.527 | 63.5531 | 64.0042 | 64.3946 | 65.0199 | 65.4866 | 66.4031 | 67.017 | 67.7186 | 68.6231 | 69.3485 | 69.9437 | 70.6541 | 71.429 | 72.2992 | 73.0881 | 73.9618 | 74.7482 | 75.7112 | 76.3747 | 77.4799 | 78.2286 | 79.0543 | 80.143 | 81.0997 | 81.9259 | 82.7726 | 83.7096 | 84.629 | 85.4874 | 86.4565
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Natural gas | 82.2749 | 85.354 | 86.3431 | 88.5281 | 88.8944 | 88.2143 | 89.3904 | 93.3086 | 98.231 | 99.3256 | 96.5927 | 100.3679 | 102.1864 | 103.8694 | 105.4199 | 107.0106 | 108.708 | 109.8969 | 111.1029 | 112.6474 | 113.745 | 114.9208 | 116.1449 | 117.6333 | 119.108 | 120.5234 | 122.0479 | 123.3983 | 124.9973 | 126.0492 | 127.7752 | 128.9116 | 130.2855 | 131.9251 | 133.3847 | 134.4233 | 135.8622 | 137.1356 | 138.5245 | 139.5734 | 141.0884
Liquids | 171.1008 | 171.8756 | 174.2848 | 176.198 | 179.0815 | 182.1159 | 186.1386 | 190.2298 | 191.6284 | 195.0037 | 177.4171 | 185.9811 | 193.1978 | 197.3116 | 200.4423 | 202.7842 | 205.1945 | 207.0828 | 209.2347 | 211.0311 | 213.0976 | 214.9349 | 216.7998 | 218.2961 | 220.3251 | 222.1539 | 223.8384 | 225.5514 | 227.1492 | 229.0065 | 230.6629 | 232.4979 | 234.2439 | 236.0902 | 237.7019 | 239.5835 | 240.9406 | 242.7524 | 244.2536 | 245.97 | 247.4363
Coal | 73.6133 | 77.4204 | 80.6992 | 79.2336 | 78.9904 | 76.9804 | 71.9071 | 72.469 | 72.6356 | 72.9373 | 71.5708 | 73.0811 | 73.9666 | 74.6962 | 75.1999 | 75.4326 | 75.9029 | 76.2667 | 76.7734 | 77.1485 | 77.7634 | 78.2107 | 78.8646 | 79.2151 | 79.8568 | 80.3847 | 80.8349 | 81.381 | 81.9372 | 82.602 | 83.2131 | 83.8495 | 84.5185 | 85.2078 | 85.8376 | 86.55 | 87.2659 | 87.9514 | 88.4969 | 89.1775 | 89.7743
Renewables | 17.2412 | 17.7662 | 18.6678 | 19.6852 | 20.048 | 20.831 | 22.0058 | 22.6803 | 23.6918 | 23.8307 | 22.401 | 24.0121 | 24.6063 | 25.1256 | 25.6068 | 26.1074 | 26.6152 | 27.1299 | 27.659 | 28.2066 | 28.7735 | 29.3188 | 29.8406 | 30.3545 | 30.865 | 31.3755 | 31.8797 | 32.3783 | 32.8782 | 33.3808 | 33.8804 | 34.381 | 34.8833 | 35.3857 | 35.8791 | 36.3769 | 36.8614 | 37.3474 | 37.8326 | 38.3399 | 38.8472
Electricity | 63.6972 | 66.0407 | 67.3852 | 69.5608 | 70.8988 | 72.254 | 74.2682 | 76.3469 | 79.4271 | 80.0833 | 77.4408 | 82.0783 | 83.6636 | 85.3232 | 86.6831 | 88.3336 | 89.62 | 91.1755 | 92.5557 | 94.2797 | 95.8374 | 97.6192 | 99.1152 | 101.0462 | 102.5783 | 104.3684 | 106.3248 | 108.1166 | 110.0051 | 111.8418 | 113.697 | 115.6043 | 117.518 | 119.4693 | 121.4749 | 123.3932 | 125.1358 | 126.7936 | 128.7137 | 130.5232 | 132.3397
End-use energy consumption by sector, world
quadrillion British thermal units
history projections
industrial
transportation
residential
commercial
End-use energy consumption by fuel, world
quadrillion British thermal units
In the reference scenario developed by the EIA, the demand of fossil fuels will continuously increase. This trend must be mandatory modified toward a sustainable development based on renewable energy sources. A new energy paradigm must be implemented to limit the average temperature increase below 1.5 °C, as agreed by the majority of worldwide Countries
6

## Slide 7: IEA scenario: Fossil fuel demand
Source: IEA 2022
According to the future scenario presented by IEA, considering the present energy policies, a peak in fossil fuel demand is expected by 2030, mainly due do the decrease of the growth of NG demand and to the reduction of the use of coal

## Slide 8: Pandemic and Ukrainian war
Energy crisis is responsible of the huge growth of inflation.
Source: IEA 2022
The transition to a clean energy paradigm is crucial to avoid such crisis in the next future.
The recent events (pandemic and Ukrainian war) are becoming the major driver toward an energy transition to a fully decarbonized paradigm. Energy security is becoming a critical issue in EU.

## Slide 9: Investiments in Clean Energy
US: Inflation Reduction Act (391 billions $ for climate change and energy)
EU: Fit for 55
Source: IEA 2022
Japan: Green Transformation Policy (1.1 trillion $ for carbon neutrality)
China: clean energy targets
India: solar revolution
According to Bloomberg in 2022
US$ billions

## Slide 10: Stated Policies EU and USA
FIT FOR 55’ package
Energy System Integration, Hydrogen, Methane, Offshore Renewable Energy, Energy efficiency, Power sector based largely on renewable sources, Secure and affordable EU energy supply, a fully integrated, interconnected and digitalised EU energy market, EU Biodiversity Strategy for 2030 establishing protected areas (30% of land and 30% of sea in Europe), Farm to Fork’ Strategy, Sustainable and Smart Mobility Strategy to cut emissions by 90% by 2050.
Aiming for at least 32% share for renewable energy and at least 32.5% improvement in energy efficiency by 2030.
GREEN DEAL
European ‘Climate Law’ enshrines the 2030 intermediate target and the 2050 climate neutrality objective into legislation, strengthening the framework for ambitious climate action.
The White House set out a target of 80% renewable energy generation by 2030 and 100% carbon-free electricity five years later.
Nuclear energy could replace nearly 80% of all coal power plants in the U.S.
Massive offshore wind turbines can produce more power on a smaller footprint.
Long-term energy storage is key for a carbon-free power grid of the future.
It will help implement the EU’s revised 2030 climate target of at least 55% in a responsible way, revising all relevant legislative measures
USA POLICIES
Biden Administration plans to eliminate fossil fuels as a form of energy generation by 2035.

## Slide 11: IEA Net Zero Emission (NZE) scenario 2050
The current trend (SPS scenario) will fail to meet the goals of NZE by 2050.
Additional policies must be implemented in order to achieve NZE by 2050.
Crucial Points
Investments in green technologies.
Emerging Countries must develop green technologies.
Availability of materials for the green technologies.

## Slide 12: Change in generation: current scenario
Coal will be rapidly replaced by renewables; a certain share of nuclear and natural gas is expected by 2030.
Source: IEA 2022

## Slide 13: Toward a fully electric energy scenario
Source: IEA 2022
Energy security issues brings to an end the growth of the NG demand. LNG will continue to play a crucial role.

## Slide 14
Technologies for NZE scenario
1.5 °C increase pathaway
Source: IRENA 2022
Energy efficiency
Carbon Capture
Energy storage (H2, P2X)
Direct utilization of renewable electricity
Decarbonization and Electrification of user demand (EV, HP)
14

## Slide 15
Green H2
Bioenergy
EV
Buildings
Energy networks
Energy Storage
The actions taken by 2030 will affect the results achieved in 2050. A radical change is mandatorily required.
Source: IRENA 2022
The transition is far from being on track to 1.5 °C
15

## Slide 16
Renewable electricity
PV and wind technologies show the best profitability, also showing the fastest increase in the installed capacity.
The total installed renewable capacity in 2021 is 3.1 TW, generating about 8.0 PWh.
Source: IRENA 2022
16
The renewable capacity installed in 2021 is lower than the one of 2020!!!!
To meet the 1.5 °C scenario, the installed renewable capacity must grow by a factor 3, by 2030
PV and wind LCOE is competitive with the one of fossil fuels.

## Slide 17
Electrification of end user demand
The share of electrification in end-use sectors like industry, buildings, transport to reach 28%, 56%, and 9% in 2030, respectively.
Source: IRENA 2022
17
World electricity demand will rise to 31 PWh by 2030
(1.3 higher with respect to 2019)

## Slide 18
Renewables will provide 65% (42 % consisting of variable RE) of the total electricity supply by 2030
Specific policies and measures such as RE targets, tax incentives, pricing mechanisms, among others are needed to increase the deployment of renewables
Huge increase of VREs: need for energy storage and/or P2X technologies
IRENA 1.5 C scenario: electricity
Source: IRENA 2022
18

## Slide 19: Smart Energy Networks
Future (smart) energy network based on renewable multigeneration systems.
Integration of several energy users
Optimization of the overall load profile, implementing suitable synergies among different energy users.
Polygeneration

Production of several energy vectors and/or byproducts.
Control strategies
Development of advanced control strategies to improve the energy efficiency of the network.

## Slide 20: A novel paradigm based on distributed polygeneration
Polygeneration, or multi-generation, is usually defined as the combined production of multiple energy vectors (e.g. electricity, cool, heat, etc) and/or products (e.g. hydrogen, methanol, etc) using natural resources (fossil fuels, wood, etc) and/or renewable energy sources (solar, wind, biomass, etc).
Simple examples are: Cogeneration and Trigeneration.
Resources
Fossil fuels:
Oil, Natural gas, Coal, etc.
Renewable energy
Sun, Wind, Biomass, etc
Natural resources
Maize, Sugar Cane, etc
Polygeneration
Products
Energy vectors:
Electricity, Cool, Heat, etc.
Energy Products:
Hydrogen, Ethanol, Methanol, Biogas, Syngas, Steam, etc
Non Energy products
Drinking water, Sugar, CO2, O2, etc

## Slide 21: Polygeneration: layouts
Biomass
Cooling
Fresh water
Fresh water
Natural gas
Power
Heat
ICE
GT, MGT
FC
STE
DHW, Heating
Thermal desalination unit
Electrical desalination unit
Electricity to user
Thermal chiller
Electrical chiller
Solar
PV
PVT
STC
Production unit
Gasifier
CC
Syngas / biogas
Methanol
Boiler
Ethanol
Coal
Fertilizer
H2
Geothermal
ORC
ST
Wind
Seawater

## Slide 22: Thermal Energy Networks: DHC
Energy Volume 68, 15 April 2014, Pages 1-11

## Slide 23: 4th generation DHC
Low operating temperature: 55-60°C supply / 25-30 °C return.
Centralized thermal energy production.
Integration of renewable energy technologies.
Use of thermal energy storages (TES) to reduce peak network flows.
Integration of HPs and low-temperature renewable sources.
Different pipings for heating and cooling
The system is not able to simultaneously match both buildings heating and cooling demands
Temperatures of heating and cooling loops are different.
The centralized production is not feasible for all the urban areas

## Slide 24: 5th generation DHC
2,000
Neutral operating temperature: -5 °C→35 °C
Bi-directional low temperature networks.
Use of hybrid substations based on reversible heat pumps.
Use of thermal energy storages (TES), in some cases.
Exchange of excess thermal / cooling energy among buildings in the network.
Users are
PROSUMERS
The system simultaneously matches both the heating and cooling demands of different buildings
The system should be installed in densely populated areas.

## Slide 25: Smart Energy Networks electrical balance
4th and 5th generation DHC, mainly based on electrical HPs
VREs (wind, PV, etc)
User load demand

## Slide 26: Smart energy networks VRE and excess renewable energy
Storage Systems
The penetration of renewables in energy networks and smart energy networks is limited by the mismatch between the renewable power production and power demand.
Electricity imported/exported to the grid should be limited to avoid a stress of the grid.
Germany

## Slide 27: Excess renewable energy
Storage Systems
Pros
Cons
mature technology
low capital cost
limited flexibility
Pros
Cons
very flexible
higher power density
not yet mature
high capital cost
Lithium-ion battery
Power to X

## Slide 28: Power-to-X: Definition
“Power-to-X processes are defined as processes with the goal to exploit the environmental and economic potential of renewable electricity”
Jannik Burre et al. – Chemie Ingenieur Technik, 2019
“the means to convert electricity, understood to be primary energy, into an energy carrier, heat, cold, product, or raw material. It is an umbrella term for different ways of generating energy, namely power-to-gas, power-to-liquid, power-to-fuel, power-to-chemicals and power-to-heat”
Michael Sterner, professor of OTH Regensburg University (GE), 2021
“the process of converting green electricity into hydrogen or PtX products based on hydrogen”
DANSK ENERGI, 2020
“the concept of Power-to-X can be further incorporated to transform the generated renewable electricity into chemical energy stored in the gas form”
Lim JY et al. – Applied Energy, 2021

## Slide 29: Power-to-X: History
First appearance of the term.
First mention to the e-fuels, which are chemicals produced starting from renewable electricity.
The terminology is a broader extending of large-scale storage systems.
Energy Conversion and Management 266, 2022, 115814

## Slide 30: Power-to-X: Overview
Renewable and Sustainable Energy Reviews 112, 2019, 865-879
DRM
RWGS
DHG

## Slide 31: e-Fuels
Fuels with net zero CO2 emissions.
Aviation sector
Maritime sector
E-kerosene: is produced from renewable electricity and captured CO2.
The H2 comes from electrolysis driven by the excess renewable energy and the CO2 is captured from the atmosphere, power or industrial plants
E-ammonia: produced do be used in blended dual-fuel engines to abate COx.
Road vehicles sector
Building sector
Fit For 55
ReFuelEU Aviation - FuelEU Maritime
European Green Deal
H2 Strategy: 40 GW electrolysers and 10 million tonnes of renewable H2 by 2030
H2-derived synthetic fuels or PtX fuels such as e-kerosene and other electrofuels.
RED II
Renewable fuels of non-biological origin (RFNBOs)
Recycled carbon fuels (RCFs) under which P2X pathways are included with hydrogen (in the case of RFNBO).

## Slide 32: e-Fuels: FuelEU Maritime
The envisaged regulatory trajectory is calculated on the basis of 2020 fuel mix resulting in a 90.3 gCO2eq/MJ 1 fleet-level baseline Well-To-Wake (WTW) fuel carbon intensity performance.
Competitiveness:
1st: fossil LNG in dual-fuel (8.5-9.3 €/GJ)
2nd: Waste-based biodiesel (2030 price 14.8-32.0 €/GJ for used cooking oil).
3rd: green ammonia (26.9-67.2 c€/GJ).
Biodiesel can be dropped-in in existing dual-fuel engines, e-ammonia requires new vessels.

## Slide 33: e-Fuels: ReFuelEU Aviation
The Commission puts forward obligations on fuel suppliers to distribute SAF when supplying fuel at EU airports, in order to enhance SAF uptake by airlines and so help reduce emissions from aviation.
The fit for 55 package includes a proposal to increase production and use of sustainable aviation fuels (SAF), also known as the ReFuelEU Aviation initiative.

## Slide 34: Power-to-Gas: Electrolysis
1.3 – 2.3 k€/kW
h 50% - 80%
4.0 – 6.0 k€/kW
h 80% - 90%
0.8 – 1.2 k€/kW
h 70% - 82%

## Slide 35
CO2 + 4H2 → CH4 + 2H2O
Exothermic reaction ∆H0298K = -206.28 kJ/mol;
Nichel-Allumina catalyst;
Catalytic methanation occurs at T > 250 °C.
Key factors
Power-to-Gas: Methanation
Methanation process combines hydrogen and carbon dioxide to produce methane and steam, according to Sabatier reaction. At the equilibrium, the production of methane is promoted at high pressure and inhibited at high temperature level.
Since catalytic reactors are not supposed to withstand temperatures higher than 550 – 700 °C, the main interest in research regards the control of the operating temperature of the process.
The heat produced by the exhotermic reaction may be recovered to support steam production in case of SOEC electrolysis.
A biological methanation process is also under investigation. The process is supported by highly specialized microorganisms (Archaea) within a technical system converting H2 and CO2 in CH4.

## Slide 36: Power-to-Gas: Methanation reactors
Fixed-bed adiabatic reactor
High internal temperature due to exotermic reaction.
Fixed-bed cooled reactor
Combines advantages of isothermal and adiabatic reactors.
Fluidized-bed reactor
Molecules fluidification comes with mechanical stress on reactor’ surface.
Tri-phase reactor
Disadvantages due to liquid-gas resistance.
Usually these reactors are modelled as plug flow reactor (PFR) to observe the temperature gradient along the reactor. The control of the process heat is crucial for these reactors.
Renewable Energy
170, 2021, 1040-1051
Energy Convers. Manage.
115, 2016, 308-326

## Slide 37: CO2 Capture
CO2 can be obtained from biomass plants, power generation plants, industrial processes and ambient air.
The most relevant CO2 sources, are these from cement manufacturing, iron and steel making, and chemical processes, in which CO2 is generated as by-product as in the process of ethylene production.
CO2 from ambient air (DAC) is technically feasible but, due to the very low partial pressure of CO2, the specific costs of the vision are very high.
Sector | CO2 sources | CO2 concentration in exhaust gas [vol%]
Biomass processes | Biomass fermentation | 15–50
 | Biogas upgrading | ≈100
 | Bioethanol production | ≈100
Power generation plants | Natural gas combustion | 3-5
 | Petroleum combustion | 3-8
 | Coal combustion | 10-15
Industrial processes | Cement production | 14-33
 | Iron and steel production | 20-30
 | Ethylene oxide production | ≈100
Environment | Ambient air | ≈0.04
Ambient Air
Biomass
Power & industrial plants
CO2

## Slide 38: CO2 Capture
The CO2 capture process in the CCS (Carbon Capture and Storage) unit could be divided into two phases: CO2 separation and CO2 compression. CO2 separation is the main part of the CO2 capture process.
International Journal of Electrical Power & Energy Systems, 143, 2022, 108503

## Slide 39: CO2 separation technologies
High CO2 capacity at high pressure but huge energy consumption.
Absorption
Adsorption
Membrane
Cryogenic
Absorption
Fast kinetics and high thermal stability but low CO2 capacity at low pressures.
Low capital costs and compact design but low gas capacity and high temperatures cause degradation of the membranes.
With amine  mature but corrosive.
With water  no corrosion but high losses.
Renewable and Sustainable Energy Reviews 81, 2018, 433-446
CAPEX = 5.5 k€/(m3/h)
CAPEX = 4-5 k€/(m3/h)
CAPEX = 4.5 k€/(m3/h)
CAPEX = 6 k€/(m3/h)

## Slide 40: CO2 Capture from Biogas
CO2 is withdrawn as a by-product of the biogas upgrading unit, which selectively separates the methane from the carbon dioxide.
The biogas is a gaseous compound obtained from the anaerobic digestion (AD) process of several types of organic biomasses.
Bio-methane
CO2
Biogas
The collected CO2 maybe combined with the H2 produced by electrolysis using the excess renewable energy, producing methane, featured by a net-zero environmental impact.

## Slide 41: Green and blue hydrogen
The hydrogen produced by renewables is called “green” whereas the one produced by fossil source is “blue” in case of CCS or “gray” without CCS.
In 2020, on 70 millions of H2 produced, only 4% was “green”.
Energy Conversion and Management 266, 2022, 115814

## Slide 42: Power-to-Liquid H2
Electrolysis reaction:
Liquid H2 is recommended for long distance transportation and large-scale consumers, where H2 compression is no more feasible.
The liquefaction process follows a Claude cycle.
The green alternative final price is 7 $/kgLH2 or in a range 2.5–4.5 $/kgLH2 because of the significant difference in electricity price. The price of green liquid hydrogen is approximately two to three times higher than the cost of conventional liquid hydrogen production from fossil fuels, including CCS 1.4–3.4 $/kgLH2.
Energy Conversion and Management 266, 2022, 115814

## Slide 43: Power-to-Liquid H2: Key factors
Roundtrip efficiency of the system:
0.35 – 0.45
Hydrogen, either in gas or liquid form, can store less hydrogen in the same volume as ammonia or methanol.
Energy density (W/cm2):
0.20 – 0.45 (generation)
0.35 – 1.15 (storage)
Energy Conversion and Management 266, 2022, 115814

## Slide 44: Power-to-Methane
Power-to-Gas could promote a rapid transition to low-carbon fuels by blending natural gas (NG) and hydrogen in existing pipelines.
Hydrogen causes embrittlement and corrosion in the natural gas pipelines, and special materials such as polyethylene should replace the steel pipelines when dealing with percentages higher than 20 % of hydrogen mixture.
the Power-to-Methane (PtM) concept is a promising option to exploit surplus renewable energy.
Renewable and Sustainable Energy Reviews 98, 2018, 302-316

## Slide 45: Power-to-Gas: CH4 & CH4-H2 blending
The methanation reaction is exothermic and its change in moles is negative, therefore the process is promoted at low temperature and high pressure.
Hydrogen can be produced at a price of 5.8–6 $/kg H2 from wind electrolysis, while hydrogen produced by the steam reforming process costs 1.25–3.5 $/kg H2.
Roundtrip efficiency of the system:
0.36 – 0. 56
Energy density (W/cm2):
0.20 – 0.45 (generation)
0.40 – 1.20 (storage)
Energy Conversion and Management 266, 2022, 115814

## Slide 46: Power-to-NH3
Haber-Bosch synthesis:
Ammonia is a promising hydrogen carrier because every molecule of ammonia (NH3) contains three hydrogen atoms.
Ammonia is currently used mainly in the agricultural industry as a fertilizer, but it is also heavily used in the refrigeration industry as a working fluid.
The long-distance transportation of hydrogen can be performed in ships powered by clean ammonia, after the development of an ammonia dual-fuel engine (2025).
Energy Conversion and Management 266, 2022, 115814
Energy Conversion and Management 266, 2022, 115814

## Slide 47: Power-to-NH3: Key factors
SPB 5 years with Haber-Bosch reactor and Solid Oxide electrolyzer technology.
Roundtrip efficiency of the system:
0.26 – 0.43
Energy density (W/cm2):
0.18 – 0.35 (generation)
0.30 – 0.80 (storage)
Energy Conversion and Management 266, 2022, 115814

## Slide 48: Power-to-methanol
In 2020, 157 million metric tons of methanol were produced worldwide, making it one of the most highly synthesized chemicals after ammonia, but it is expected to equal ammonia production in 2030.
It is mainly used for producing other chemicals, such as formaldehyde, acetic acid, and plastics, but smaller quantities are also used as fuel for vehicles, ships, industrial boilers, and cooking.
Energy Conversion and Management 266, 2022, 115814

## Slide 49: Power-to-methanol: Key factors
SPB < 5 years for biomass integrated with SOEC plants.
Roundtrip efficiency of the system:
0.33 – 0.45
Energy density (W/cm2):
0.17 – 0.38 (generation)
0.40 – 0.90 (storage)
Energy Conversion and Management 266, 2022, 115814

## Slide 50: Power-to-Heat
P2H using excess variable renewable energy (VRE) may be used to supply heat by electric boilers or HPs.
Applied Energy 212, 2018, 1611-1626

## Slide 51: Power-to-Heat: Applications
Power to heat conversion is far from the location of the demand (storage is mandatory).
Power to heat conversion is close to the location of the demand (storage may be not necessary).
Thermal Energy Storage (TES) can play a crucial role in achieving future decarbonization goals in Europe, especially in a highly renewable energy integrated system.
Applied Energy 212, 2018, 1611-1626

## Slide 52: Power-to-Heat Classification
Sectors:
households and TCS (trade, commerce, and service)
industry and process heat
district heating.
Temperature
low (<120°C)
medium (120-1000°C)
high (>1000°C)
Technologies
Electric heat pumps
Electric resistance heaters
Sustainable Energy Technologies and Assessments, 53, 2022, 102553

## Slide 53: Power-to-Power
Electrolytical conversion of renewable power surplus into hydrogen and, or, chemicals. Electrochemical conversion of chemical storage into available power.
Gaseous Hydrogen is the most adopted chemical storage option, by means of several technologies.
Reducing the cost of SOECs will likely require a combination of different approaches, including materials development, manufacturing improvements, stack design, energy efficiency, and government policies.
International Journal of Hydrogen Energy, February 2023

## Slide 54: Power-to-Power: Storage
The energy density of hydrogen is extremely low even at 300 bar.
Hydrogen storage technologies
Only liquid (cryogenic) or solid (metal hydrides) storage would make a difference.
These processes are either highly energy demanding or not suitable for large-scale hydrogen storage.
International Journal of Hydrogen Energy, 47, 2022, 17505-17525

## Slide 55: Power-to-Power: Gaseous H2
Hydrogen compression
Compression from 1 to 1000 bar requires twice as much work as compression from 30 to 1000 bar, 4 kWh/kgH2 and 2 kWh/kgH2, respectively.
Increasing the stages leads to a reduction of compression work because the process gets closer to isothermal.
For n stages, non-isentropic compression increases the total compression work.
International Journal of Hydrogen Energy, 47, 2022, 17505-17525

## Slide 56: Power-to-Power: Liquid H2
Hydrogen liquefaction
Liquefaction of hydrogen can be divided into four general stages:
Precompression (ambient conditions).
Precooling (ambient to about 80 K).
Cryo-cooling (80 K - 30 K).
Liquefaction (30 K to LH2 at atmospheric pressure).
Total power consumption of conventional H2 liquefaction plants is about 13 kWh/kgH2 (≈40% of H2 LHV).
For advanced arrangements this consumption can be roughly halved.
International Journal of Hydrogen Energy, 47, 2022, 17505-17525

## Slide 57: Power-to-Power: Solid H2
Hydrogen metal hydrides (MH)
The combination of metals or alloys with hydrogen leads to the formation of metal hydrides.
During loading, hydrogen is adsorbed through an exothermic reaction. Conversely, hydrogen is released (desorbed) when heat is supplied to the metal hydride.
The adsorption/desorption processes make use of cooling and heating sources. These reservoirs are at temperatures of ~10°C for cooling and ~50°C for heating, even though this depends on the specific MH chosen.
Metal hydrides density is higher than 115 kgH2/m3.

## Slide 58
Power-to-Power: Fuel Cells
 | Low temperature fuel cells |  |  | High temperature fuel cells |  | 
 | AFC (Alkaline) | PEFC (Proton Exchange) | PAFC (Phosphoric Acid) |  | MCFC (Molten Carbonate) | SOFC (Solid Oxide)
Temperature (°C) | 60-120 | 70-100 | 160-220 |  | 600-650 | 800-1000
Pressure (bar) | - | 1.5-4 | - |  | - | -
Electrodes | PFTE e noble metals | Graphite | PFTE |  | Nichel | LMS, Ni,ZnO2
Electrolyte | KOH | Polymer membrane | H3PO4 |  | Alkaline metals carbonate (CO32-) | Yttrium-stabilized Zirconia
Catalyst | Pt, Pd, Ag, Ni | Pt | Pt |  | Ni | -
Charge carrier | OH- | H- | H- |  | CO32- | O2-
Electric efficiency (LHV) (%) | 60 | 40-50 | 40-50 |  | 45-55 | 45-60
Power density (mW/cm2) | 300-500 | 300-900 | 150-300 |  | 150 | 150-270
Materials | Plastic, graphite, Inconel | Graphites, metals | Graphites |  | Nichel, inox | Ceramics, metals
State of art | Small power plants | Advanced experimentals | Demonstrative plants up to 11 MW |  | Demonstrative plants up to 2 MW | Demonstrative plants up to 0.30 MW
Pros | High power density | High power density, non volatile electrolyte, fast starting up | High efficiency in CHP, mature technology |  | High temperature heat, high efficiency, possibility of internal reforming | High temperature heat, high efficiency, catalysts not necessary
Cons | No tolerance to CO, high purity of input fuel | Low tolerance to CO, water management problem | Low tolerance to CO |  | Life and stability problems, CO2 reicirculation required | High thermal stress, slow starting up

## Slide 59
GRETHA Project
A project for the polygeneration based on the green hydrogen production
Objectives
A novel paradigm based on the fuel cells and green hydrogen in order to obtain the production of electric, thermal and cooling energy for several users.
The energy transition based on the distributed energy systems at low environmental impact.
A system aims at reducing the energy dependency from foreign countries.
The development of innovative storage systems based on high energy density and competitive costs technologies.
The production from renewable energy sources in order to drastically limit the electricity from the grid.

## Slide 60
GRETHA Project
A project for the polygeneration based on the green hydrogen production
Layout
The project aims at developing a novel trigeneration system based on PV panels, a high temperature PEM fuel cell, electrolyzer for green hydrogen production, a biomethane reforming unit, an ACH, hydrogen vehicles and a metal hydrides storage system.

## Slide 61
Development of a dynamic calculation tool for energy and economic simulation and optimization of the research prototype to predict its operation for any plant configuration, for different users and for any possible weather zone.
Experimental investigation: the most important result of the research and development activities will be the design, construction, installation and experimental test of the proposed system. The measurements performed during the tests will be able to carefully monitor all the operating parameters and environmental effects in order to validate the benefits expected from the proposed technology
Development of prototype design standards considering that the innovation of the proposed system innovative system. In particular, there are no specific methods for the design of the components, nor defined procedures for the authorization of the processes and/or for the management of the whole plant.
A project for the polygeneration based on the green hydrogen production
Results
GRETHA Project

## Slide 62
Research Projects: Power-to-Power
Power-to-power technology based on reversible SOFC
The layout is compared with the mature lithium-ion battery storage technology.

## Slide 63
Research Projects: Power-to-Heat
Power-to-heat technology based on 5th generation DHC integrated with photovoltaic system
Simultaneous heating and cooling demands at the same time.

## Slide 64
Research Projects: Power-to-Gas
Power-to-gas technology based on PV and solid oxide electrolyzer
The hydrogen is produced by means of solid oxide electrolysis and the carbon dioxide is obtained as a by-product of the biogas upgrading process.

## Slide 65: Conclusions
The World is far from being on track to achieve the goal of 1.5°C temperature increase
A novel energy paradigm must be mandatory implemented, based on smart energy networks and renewable
In the future scenario a massive electrification of user demand is expected, also considering the use of HP and 4° and 5° generation DHC
A dramatic increase of the VRE (mostly wind and PV) is expected pointing out the issue of the mismatching between renewable production and user demand
P2X technology will play a crucial role, converting the excess renewable production in: methane, hydrogen, efuels, heat, chemicals, etc. It can be also used as electrical storage
The integration of P2X in existing and novel smart energy networks is crucial to optimize system performance and to achieve a reasonable economic profitability

## Slide 66
Thank you for your attention!