## Slide 1: Renewable Energy Systems: Current Status in the World Prospects and Problems Soteris A. Kalogirou
Cyprus University of Technology
Department of Mechanical Engineering and Materials Sciences and Engineering
Editor-in-Chief, Renewable and Sustainable Energy Reviews
Editor-in-Chief Emeritus, Renewable Energy
Honorary Editor, Energy
Fellow of the European Academy of Sciences
Founding Member of the Cyprus Academy of Sciences , letters, and Arts
Member Academia Europaea
Fellow of CORE Academy of sciences and Humanities
IF 9.1 (2025)
IF 9.4 (2025)
IF 16.3 (2025)

## Slide 2: Outline
Introduction – Climate change
Status of Renewables
  Solar thermal
  Photovoltaics
  Hydro Power
  Wind Energy
  Biomass
  Other technologies
Prospects – New research
Problems associate to RES

## Slide 3: Convincing Evidence
Melting polar ice caps
Hurricane Katrina
Coastal flooding - UK
Germany flooding
Melting polar ice caps
Switzerland flooding
Notes: 3
Aerial view of Kuwait fires

## Slide 4
The term Climate Crisis represents better the situation instead of Climate Change
or Global Warming
Climate refugees
Effect of Climate Change
Flooding in India - 2020
Flooding in Germany - 2021

## Slide 5: Temperature anomaly and CO2 concentration From Vostok ice-cores (East Antarctica)
Notes: 5

## Slide 6: CO2 in the last 1000 years
Industrial revolution
Current value: www.co2now.org
Notes: 6

## Slide 7: Conventional Fuels – Reserves (end of 2020)
Coal ~ 139 Years
Crude Oil ~ 53.5 Years (because of shale oil)
Natural Gas ~ 48.8 Years
  * BP Statistical Review of World Energy 2021, 70th Edition
Biggest problem: Environmental issues related to the use of these fuels – China & India are the most polluting countries

## Slide 8: Renewable Energy Systems
Solar power (solar thermal & PV)
Hydro systems
Wind energy systems
Biomass-Biogas-Biofuels

## Slide 9: Renewable Energy Indicators 2024
Source: Renewables 2025: Global Status Report, REN21

## Slide 10: 2024 data…
A record 741 GW of renewable power capacity added in 2024!
  By far the largest annual increase today.
  PV accounted for more than three-quarters of that growth – due to falling technology costs and rising demand.
  Problem: While renewable deployment is increasing, system transformation is not progressing so fast.
In developing countries rooftop PV grew 22%  clearly indicating a shift towards decentralised energy systems.

## Slide 11: Total Final Energy Consumption by Source
Source: Renewables 2025: Global Status Report, REN21

## Slide 12: Electricity Generation by Energy Source 2015-2023
Source: Renewables 2025: Global Status Report, REN21

## Slide 13: We need to do more…..
Go beyond the power systems – heat and fuels account for more than three-quarters of total energy consumption.
  Renewables only meet 5.7% of this demand
  Renewables in transportation need to substantially increase
  Electrification across end use is slow and uneven across sectors
Long-term energy planning and institutional reform are needed to enable economy-wide energy transition and accelerate the shift towards renewables.
Positive sign: Record global EV sales, representing more than 1 out of 5 car sales in 2024.

## Slide 14: Countries with High Shares of Wind and Solar Generation in Their Power Systems, 2024
Source: Solar Heat Worldwide: Global Market Development and Trends in 2024, Edition 2025

## Slide 15
Source: Solar Heat Worldwide: Global Market Development and Trends in 2024, Edition 2025

## Slide 16: Global Levelized Cost of Electricity (LCOE) for utility scale RES 2010-2021
Source: Renewables 2022: Global Status Report, REN21

## Slide 17: Global Investment in New Power Capacity by type 2024
Source: Renewables 2025: Global Status Report, REN21
Investment in 2024 reached 728 billion USD but remain concentrated in China, EU and the US.
Only 6% goes to
investment on other technologires

## Slide 18: Global Renewable Energy Employment, by Technology, 2017-2023
Source: Renewables 2025: Global Status Report, REN21

## Slide 19: Warning!
Although we are deploying renewables in record numbers we are not building the systems needed to transition to a renewable-based economy.
Need:
  Coherent policies,
  Coordinated planning, and
  Resilient infrastructure including mainly grids and storage.
    Example: PV-EV chargers can help to reduce grid loading and improve stability
Renewables must be treated as core economic infrastructure which is essential for energy security, resilience and prosperity.
Need to align policies and planning the soonest, to support a full transformation of economies and soceities.

## Slide 20: Solar Thermal Power
Systems utilising either the thermal radiation or the light of solar irradiance.
Solar thermal systems
  Low temperature systems (mostly for water heating and industrial processes)
  High temperature systems (mostly for CSP and high temperature industrial processes)
Solar photovoltaics

## Slide 21: Low temperature collectors
Flat plate collectors
Evacuated tube collectors
Compound parabolic
collectors

## Slide 22: Solar Water Heating Collectors Global Capacity, 2015–2024
Source: Renewable 2025: Global Status Report, REN21

## Slide 23: Solar water heating in Cyprus A success story
93% of all houses in Cyprus have a SHW – world record

## Slide 24: Research led to several new innovations
Use of polymeric materials for the manufacture of solar thermal absorbers to:
  reduce cost due to lower raw material and manufacturing costs.
  reduce weight compared to copper or aluminium.
New transparent covers with anti-reflective coatings for high optical transmission.
Development of new selective absorber for high absorptance and low emission coatings.
Vacuum insulation for flat-plate collectors  use of high vacuum or noble gases

## Slide 25: High temperature systems
Parabolic trough collector
Linear Fresnel collector
Solar dish
Solar tower
Gemasolar
Solar Two

## Slide 26: Concentrating Solar Thermal Power Global Capacity, by Country/Region, 2016–2024
Source: Renewables 2025: Global Status Report, REN21
Many CSP systems are under development in many countries of the world
All new facilities incorporate thermal ENERGY STORAGE

## Slide 27: Biggest CSP: Noor Ouarzazate Solar Complex, Morocco (2018), rated capacity: 510 MW, and thermal storage capacity of 3005 MWh, enabling a discharge of 5.9 hours

## Slide 28: Industrial Process Heat-Solar Juice
• Parabolic trough collector (PTC)
-96 m collector length (2×48 m rows)
-Aperture 3 m (mid-size)
-Oil temperature: 425°C
• Concrete Thermal Energy Storage
-Capacity: 600 kWh
-2 modules (each 300 kWh)
-Each module consists of 2 concrete blocks
-Length per block: 5 m
Storage and plantroom containers Concrete storage

## Slide 29: Photovoltaics
Four basic technologies:
  Polycrystalline silicon cells
  Monocrystalline silicon cells
  Amorphous silicon cells
  Other thin film cells

## Slide 30: Solar PV Global Capacity and Annual Additions, 2015-2024
Source: Renewables 2025: Global Status Report, REN21

## Slide 31: Solar PV Global Capacity, Top 10 countries and Rest of the World, 2024
Source: Renewables 2025: Global Status Report, REN21

## Slide 32
Kurnool Ultra Mega Solar Park, India – 1000 MW, 2017
Current PV Research:
Higher performance cells/modules
New nanomaterials applications
Advanced manufacturing techniques
Trend towards very large systems
Notes: 32

## Slide 33
The largest solar power plant in the world right now.
Installed in Zhongwei, Ningxia.
Tengger desert (Inner Mongolia).
The area of the solar field is 1,200 km2
Tengger Desert Solar Park – 1547MW – China

## Slide 34: Hydro Power
Comes in a variety of sizes:
Large Hydro (>10 MW)
  18 GW scheme at the Three Gorges, China (largest) now expanded to 70 GW
  An example of Large Hydro ( > 10 MW)
Small Hydro (1 – 10 MW)
Mini Hydro (100 kW – 1 MW)
Micro Hydro (< 100 kW)
And finally, Pico Hydro (< 5 kW)…

## Slide 35: Hydropower Global Capacity, Shares of Top 10 Countries and Rest of World, 2024
Source: Renewables 2025: Global Status Report, REN21

## Slide 36: Wind Power

## Slide 37: Wind Power Global Capacity and Annual Additions, 2015–2024
Source: Renewables 2025: Global Status Report, REN21

## Slide 38: Biomass
Main areas:
  Biomass
  Biogas
  Biofuels (biodiesel)
  Waste (MSW, landfills [?])

## Slide 39: Biomass – Question food for fuel?
Three years poplar cropping
(ENERGY crops)
 Land availability for energy crops

## Slide 40
More than 90% of transport depends on oil, US consumption of its 200 million cars is 3.5 million barrel of oil per day  Prospects for biofuels
Notes: 40

## Slide 41: Shares of Bioenergy in Total Final Energy Consumption, Overall and by end-use sector, 2022
Source: Renewables 2025: Global Status Report, REN21

## Slide 42: Global Production of Ethanol, Biodiesel and Renewable Diesel 2014-2023
Source: Renewables 2025: Global Status Report, REN21

## Slide 43: Other areas of renewables
Ocean energy systems
  Wave, tidal energy conversion, OTEC
  Total capacity: 513 MW (2024)
Geothermal
  Global capacity: 15.1 GW (2024)
Hydrogen
Used both for storage and Fuel Cells

## Slide 44: PV powered EV Charging
PV powered EV charging stations, combine onsite solar electricity generation with EV charging infrastructure, are a sustainable solution for electric vehicle adoption, offering several benefits:
  Reduction in Greenhouse gas emissions (clean PV electricity).
  For house PV systems close to zero transportation cost.
  Smart Charging Control: Possibility to apply smart charging strategies like V2G services, which enhance grid flexibility and maximise solar energy utilisation.
  Possibility for integration with microgrids providing a more efficient and sustainable energy solutions.
  At a bigger scale there are specific challenges for charging Electric Busses with solar energy which offer the potential for these stations to drive sustainable mobility.

## Slide 45: Hydrogen busses: The Future of Clean Public Transport
Hydrogen fuel cell buses are a promissing solution for urban trnsportation, offering zero-emission operation and ability to cover long distances without frequent refueling.
Refueling is a quick process-advantage over EV charging.
Routes within cities eliminate potential hazards because of the use of hydrogen.

## Slide 46: Prospects - Hot research areas
Main purpose:
  Increase efficiency of various RE technologies
  Design renewable energy components at lower cost
Extensive use of RES (many regions, even countries consider transformation into 100% renewables)
  High shares of renewables
  Power system transformation
  Storage/integration (smart energy systems)
  Develop large-scale smart regions – like smart cities
Effective coupling not only for electricity but also heating + cooling and transportation

## Slide 47: Acknowledgements
Main reports used for this survey:

## Slide 48
Soteris Kalogirou
email: soteris.kalogirou@cut.ac.cy
Concluding:
There are a lot of possibilities to utilise effectively renewable energy technologies
These are nowadays more cost-effective options than conventional fuels
We should never underestimate the climate problem
It is in our hands to utilise renewables effectively

## Slide 49: Final conclusions
The energy transition is an oportunity to transform our countries economies.
Renewables can be viewed as catalysts of system change but need governments to align behind long-term strategies.
Conclusion: Governments, industry and international institutions need to move beyond deployment targets and commit to system wide reform which should include:
  Long-term energy planning
  Modernising grids
  Investment in storage
  Reducing energy consumption
  Eliminate financial barriers
  Moving away from fossil fuels and accelarate shift to a reneable-based economy.

## Slide 50: Thank you for your attention
I will be happy to answer questions…